## Slide 1: Control Systems Overview

## Slide 2
Introduction and Overview of Control System

## Slide 3: Physical System to Time Domain
The laws of the Natural and Physical world are usually written and modeled in the form of differential equations .
Functions are not equations. They are statements. They become equations, if some of the magnitudes in them are known (the independent variables) and some are unknown (the dependent variables), and we want to find the value of the latter by performing on the former the operations in the function.
A differential equation is a mathematical equality that relates some function(s) with its (their) derivatives.
Fig: Equivalent Circuit of DC Motor
Image Source: https://ctms.engin.umich.edu/CTMS/index.php?example=MotorSpeed&section=SystemModeling

## Slide 4: Time Domain Analysis
DC motor have constant dynamical behavior (time-invariant) and can be modeled by linear differential equations. Motors are usually modeled as LTI systems for analysis and design.
In time-domain analysis the response of a dynamic system to an input is expressed as a function of time c (t).
It is possible to compute the time response of a system if the nature of input and the mathematical model of the system are known.
The time response of a system can be obtained by solving the differential eq. governing the system.
Alternatively, the response c(t) can be obtained from the transfer function of the system and the input to the system.
For specifying the desired performance characteristics of a measurement control system.
These characteristics of a system of any order may be specified in terms of transient response to a unit step input signal.
Fig: Differential systems form a subset of continuous-time LTI systems.
Image Source: https://www.globalspec.com/reference/62550/203279/chapter-3-differential-and-difference-lti-systems

## Slide 5: Time Domain Analysis
Disadvantages:
Main limitation of time domain analysis is that the a) noise and b) disturbance characteristics are not understood as good as it is understood in frequency domain analysis. Time domain analysis is completely mute on overshoot and 3dB system response. Hence not so robust. Plus, the design is also not so easy and usually consists of heat and trial types.
Advantages:
But, in Time Domain, Interpretation is direct. It works on more accurate mathematical model that are well visualized. Stability analysis: Two most pronounced methods are- Root locus and Routh Hurtwitz criteria. Performance Parameter are: Poles - Zeros location, Rise time, Peak time, Settling time, Delay time, Damping factor, Natural and Damped frequency

## Slide 6: Frequency Domain Analysis
In the frequency domain, a linear time-invariant system acts as a filter on the frequency spectrum of the input signal, attenuating it at some frequencies while amplifying it at other frequencies. This property is called the frequency response of the system.
Frequency domain analysis replaces the measured signal with a group of sinusoids which, when added together, produce a waveform equivalent to the original.
Frequency Domain Specifications
  Resonant Peak- Maximum value of the closed loop transfer function.
  Resonant Frequency- Frequency at which resonant peak occurs.
  Bandwidth- range of frequencies for which the system normalized gain is more than -3db.
  Cut-off rate- It is the slop of the log-magnitude curve near the cut off frequency.
  Gain Margin- The value of gain to be added to system in order to bring the system to the verge of instability.
  Phase Margin- Additional phase lag to be added at the gain cross over freq. in order to bring the system to the verge of instability.
Fig: Bode Plot of DC Motor
Image Source: https://ctms.engin.umich.edu/CTMS/index.php?example=MotorSpeed&section=SystemModeling

## Slide 7: History of Frequency Domain Analysis
When dealing with the electronic amplifiers instability, the Bell Laboratory team could not find any explanation by time analysis. They just noticed that unexpectedly, amplifiers begin to whistle under certain conditions. The explanation turned to be very logical when Hendrik Wade Bode used the frequency analysis, by means of his well-known frequency diagrams (see the Barkhausen criterion).
Solving manually differential equations is difficult. These manipulations may be performed much easier if using the operational calculus (mainly Laplace). The complex variable s = σ + j ω happens to include the frequency ω! You can find an obvious physical significance to the transfer function (the main frequency analysis tool) if you compare it with the frequency diagrams (for σ = 0).
The complex generalization of the Bode frequency diagrams was proposed by his colleague Harry Nyquist, who extended the electronic amplifier frequency analysis over the whole System Theory. One perfect example for the utility of this approach is the Nyquist stability criterion.

## Slide 8: Frequency Domain Analysis
Advantages
- Stability of closed loop system can be estimated
- Transfer function of complicated systems can be determined experimentally by frequency tests
- Effects of noise disturbance and parameter variations are relatively easy to visualize.
- Analysis can be extended to certain nonlinear control systems.
Disadvantages
- They struggle with nonlinear phenomena and lose the time information. They tend to scale poorly with problem size compared to time-domain methods. That is, at some large size the frequency-domain approach will be slower than the time-domain approach.
Fig: Time to Frequency Domain Representation
Image Source: https://www.tutorialspoint.com/principles_of_communication/principles_of_communication_analyzing_signals.htm

## Slide 9: State Space Analysis
The drawbacks associated with the conventional method are as follows:
In the transfer function approach during analysis, the initial conditions are considered to be 0. However, this is not the case with state variable analysis because it considers all the initial conditions associated with the elements of the control system. And the consideration of initial conditions provides a more precise response. Hence the consideration of all the initial conditions associated with the system in the state model serves as a major advantageous factor.
The transfer function approach shows inconvenience towards the analysis of multiple input multiple output systems. As against the state variable approach supports analyzing both SISO as well as MIMO systems.
Due to the effectiveness in analyzing linear and non-linear as well as time-varying or time-invariant systems, the state-space approach is better than the transfer function approach which is applicable to linear time-invariant systems.

## Slide 10: State Space Analysis
The drawbacks associated with the conventional method are as follows:
As the transfer function approach is a frequency domain analysis thus it offers difficulty in finding the time domain solutions in case of a higher-order system. Whereas state space analysis is a time-domain approach.
The transfer function approach uses some standard test input signals for the analysis of the system, while this is not the case of state-space analysis.
As the state variable approach is associated with matrix/vector modeling thus is considered as an efficient computational approach. Hence it facilitates accurate response thus is applicable to dynamic systems.
Thus, we can say state-space analysis overcomes the limitations of the transfer function approach. Thus, we can say state-space analysis overcomes the limitations of the transfer function approach.

## Slide 11
Proportional Controller

## Slide 12: Introduction:
It is a type of linear feedback control system in which a correction is applied to the controlled variable which is proportional to the difference between the desired value (setpoint, SP) and the measured value (process variable, PV).
In other words, it can also be said as the multiplication product of the error signal and the proportional gain.
Where,
: Controller output with zero error.
: Output of the proportional controller.
: Proportional gain.
: Instantaneous process error at time t. =SP-PV.
SP: Set Point.
PV: Process Variable

## Slide 13: Introduction:
The proportional controller produces an output, which is proportional to error signal.
Applying Laplace transform on both the sides:-
Transfer function of the proportional controller is
Where,
is the Laplace transform of the actuating signal
is the Laplace transform of the error signal
is the proportionality constant

## Slide 14: Block Diagram
The proportional controller is used to change the transient response as per the requirement.
Advantages of Proportional Controller
  The proportional controller helps in reducing the steady-state error, thus makes the system more stable.
  The slow response of the overdamped system can be made faster with the help of these controllers.
Disadvantages of Proportional Controller
  The controller also increase the maximum overshoot of the system.

## Slide 15
Integral Controller

## Slide 16: Introduction:
The main purpose of the integral controller is to increment or decrement the controller's output over time to reduce the error, till the error is present in the system.
In an integral controller output is directly proportional to the integration of the error signal.
By using Laplace transform we have,
So, the transfer function of the integral controller is .

## Slide 17: Block Diagram
The integral controller is used to decrease the steady state error.
Advantages of Integral Controller
  The Controller can return the controlled variable back to the exact set point following a disturbance that’s why these are known as reset controllers.
Disadvantages of Integral Controller
  It tends to make the system unstable because it responds slowly towards the produced error.

## Slide 18
Derivative Controller

## Slide 19: Introduction:
The derivative controller produces an output, which is derivative of the error signal.
Controllers are used to improve the performance of control systems.

## Slide 20: Transfer Function and Block Diagram:
Advantages:
The major advantage of a derivative controller is that it improves the transient response of the system.
Disadvantages
It never improves the steady-state error.
It produces saturation effects and also amplifies the noise signals produced in the system.

## Slide 21
P-I CONTROLLER

## Slide 22: Introduction:
PI controller stands for propotional integral controller.
• P-I controller is mainly used to eliminate the steady state error resulting from P controller.
• This controller is mostly used in areas where speed of the system is not an issue.
• it is a combination of proportional and an integral controller the output (also called the actuating signal) is equal to the summation of proportional and integral of the error signal.

## Slide 23: Block Diagram
A proportional and integral controller output is directly proportional to the summation of proportional of error and integration of the error signal.
Where, Ki and kp proportional constant and integral constant respectively.

## Slide 24: Advantages & Disadvantages of P-I Controller
Advantages of P-I Controller
Easy to implement
Minimizes fluctuations
Has high loop gain
Disadvantages of P-I Controller
No fine controlling
Presence of offset error
Damping ratio is reduced which leads to increase in overshoot

## Slide 25
P-D CONTROLLER

## Slide 26: PD Controller
The proportional derivative controller produces an actuating error signal, which is the combination of the proportional error signal and derivative of the error signal. Control system with a proportional derivative controller is:

## Slide 27: Analysis PD Controller
From the closed loop transfer function it is observed that the PD - controller introduces a zero in the system and increases the damping ratio .
The addition of the zero may increase the peak overshoot and reduce the rise time . But the effect of increased damping ultimately reduces the peak overshoot .
From the loop transfer function it is observed that the PD - controller does not modify the type number of the system . Hence PD - controller will not act modify steady state error

## Slide 28: Advantages, Disadvantages and Applications.
Advantages of Proportional Derivative Controller
a ) Improving the Gain Margin , Phase Margin , Peak overshoot .
b ) Improves the stability of the system without affecting the steady - state error .
c )Can handle changes in fast load as the load change offset error is acceptable .
d ) Reduces rise time settling time .
Disadvantages of Proportional Derivative Controller
a ) Cannot eliminate the offset error of proportional controller
b ) Damping ratio is increased
c ) Attenuates high - frequency noise .
Applications of Proportional Derivative Controller
a ) Used in DC motor position control .
b ) Used for tuning of fractional order controllers .
c ) Works as high pass filter

## Slide 29: References
Physical System
https://www.researchgate.net/post/What_is_the_physical_significance_of_frequency_domain_analysis_of_control_system
https://www.quora.com/What-is-the-need-to-convert-a-time-domain-signal-to-a-frequency-domain-signal-and-vice-versa
https://www.quora.com/What-are-the-real-world-applications-of-Laplace-transform-especially-in-computer-science
https://resources.pcb.cadence.com/blog/2020-time-domain-analysis-vs-frequency-domain-analysis-a-guide-and-comparison
https://ctms.engin.umich.edu/CTMS/index.php?example=MotorSpeed&section=SystemModeling
https://www.quora.com/How-might-differential-equations-be-useful
https://www.globalspec.com/reference/62550/203279/chapter-3-differential-and-difference-lti-systems
https://www.ijert.org/time-and-frequency-domain-analysis-of-signals-a-review
https://www.eetimes.com/frequency-domain-tutorial-part-2-complex-signals-and-spectral-diagrams/
Proportional Controller
https://www.tutorialspoint.com/control_systems/control_systems_controllers.htm

## Slide 30: References
Integral Controller
https://www.tutorialspoint.com/control_systems/control_systems_controllers.htm
Derivative Controller
https://www.electrical4u.com/types-of-controllers-proportional-integral-derivative-controllers/#What-is-a-Controller
P-I Controller
https://www.slideshare.net/karansati/p-pi-and-pid-controller
P-D Controller
Control System by nagoor kani